## Slide 1: Data-Link Layer: An Introduction
Covers Chapter# 09 from Text Book
Computer Communication & Networks
(CEN-223)
Fall 2022 (BSE-5A)

## Slide 2: Logical Connections
In communication at the data-link layer:
  One data-link layer is involved at the source and one at the destination.
  Two data-link layers are involved at each router since Intermediate nodes need to both encapsulate and decapsulate.

## Slide 3: Logical Connections (Cont.)
Q) Why need both encapsulation and decapsulation at each intermediate node?
Each link of the intermediate node may use different protocol, hence the requirement for different frame format.
Even when links use the same protocol, encapsulation and decapsulation are still needed since the link-layer addresses are different.

## Slide 4: Sublayers
The data-link layer is divided into two sub-layers:
  Data-link control (DLC), deals with all point-to-point and multipoint links (broadcast links).
  Media access control (MAC), deals with broadcast links.

## Slide 5: Addressing
The source and destination IP addresses define communication between two ends but cannot define the links which the data should pass through.
The datagram is encapsulated into a frame, where two data-link layer addresses are added.
Types of link-layer addresses:
  Unicast Address: one-to-one communication.
  Multicast address: one-to-many communication.
  Broadcast address: one-to-all communication.

## Slide 7: Address Resolution Protocol
Address Resolution Protocol (ARP): is an auxiliary protocol defined in the network layer that maps the IP addresses into a link-layer address.
Q) Why do we need the ARP protocol?
Any time a node has an IP datagram to send to another node in a link, it has the IP address of the receiving node.
However, the IP address of the next node is not helpful in moving a frame through a link, where we need the link-layer address of the next node. For that, ARP is used.

## Slide 8: Address Resolution Protocol (Cont.)
If host/router needs to find the link-layer address of another host/router in its network:
Send an ARP request packet through broadcast.
ARP request packet includes: (link-layer and IP addresses of sender) and (IP address of receiver).
Every host/router that receives ARP request processes the packet.
Only intended recipient sends back an ARP response packet through unicast.
ARP response packet includes (recipient IP and link-layer addresses)

## Slide 10: Data-Link Layer: Media Access Control (MAC)
Covers Chapter# 12 from Text Book

## Slide 11: Media Access Control (MAC)
Protocols designed to handle access to shared link belong to the MAC sublayer, and can be categorized into three subgroups:

## Slide 12: Channelization
Channelization: is channel partitioning and a multiple access method in which available bandwidth of a link is shared in frequency, time or through code among different nodes.
Three channelization protocols are:
Frequency-division multiple access (FDMA)
Time-division multiple access (TDMA)
Code-division multiple access (CDMA)

## Slide 13: CDMA
In CDMA, only one channel occupies the entire bandwidth and all nodes can send data simultaneously.
CDMA means communication with different codes.
For the example, we say that:
  is data from node 1, while is the code assigned to node 1.
  is data from node 2, while is the code assigned to node 2 …. and so on.

## Slide 14: CDMA (Cont.)
In CDMA, each node is assigned a code, which is a sequence of numbers called chips.
These sequences are carefully selected (called orthogonal sequences).
In orthogonal sequences, each sequence is made of N elements, where N is number of possible nodes.
If a node is sending bit 0, it encodes it as -1.
If a node is sending bit 1, it encodes it as +1.
If a node is idle, it sends no signals, which is interpreted as 0.

## Slide 15: CDMA (Cont.)
Chip sequences
Data representation in CDMA

## Slide 16: CDMA (Cont.)
Arithmetic rules of orthogonal sequence:
When multiplying a sequence by a scalar value, every element in sequence is multiplied by that scalar value.
2  [+1 +1 -1 -1] = [+2 +2 -2 -2]
When multiplying two equal sequences, every element is multiplied by its corresponding element. Adding the multiplication results would generate the value N.
[+1 +1 -1 -1]  [+1 +1 -1 -1] = +1 +1 +1 +1 = 4

## Slide 17: CDMA (Cont.)
When multiplying two different sequences, every element is multiplied by its corresponding element. Adding the multiplication results would generate the value 0.
[+1 +1 -1 -1]  [+1 +1 +1 +1] = +1 +1 -1 -1 = 0
When adding two sequences, every element is added to its corresponding element. This would generate another sequence.
[+1 +1 -1 -1] + [+1 +1 +1 +1] = [+2 +2 0 0]

## Slide 18: CDMA (Cont.)

## Slide 19: CDMA (Cont.)

## Slide 20: CDMA (Cont.)
If a node wants to receive data of node 1, it multiplies the received composite data by node 1’s code and divides by N, as given below for the case of network of N = 4:

## Slide 21: CDMA (Cont.)
For getting Node 1’s data:
)
(the result is divided by N = 4)
 decoded to (0)
0

## Slide 22: CDMA (Cont.)
Walsh table is a two dimensional table with equal number of rows and columns.
Walsh table is used to generate the code sequences, where each “row” is a sequence.

## Slide 23: CDMA (Cont.)
Q) Two stations and received the composite signal:
[-1 -1 -3 -3 +3 -1 +1 -3]
Provided the two codes below, what are the received data at these two stations?
For , [+1 -1 -1 +1 +1 -1 -1 +1]
For , [+1 +1 +1 +1 -1 -1 -1 -1]

## Slide 24: Thank You!