## Slide 1: Data-Link Layer: Error Detection & Correction
Covers Chapter# 10 from Text Book
Computer Communication & Networks
(CEN-223)
Fall 2022 (BSE-5A)

## Slide 2: Types of Errors
Transmitted bits are subject to unpredictable changes, because of several factors including interference.
Single-bit error: means that only 1 bit of a given data unit is changed, either from 1 to 0 OR from 0 to 1.
Burst error: two or more bits in a given data unit have changed.
Single-bit error
Burst error

## Slide 3: Redundancy and Coding Techniques
Redundancy: extra bits sent with the data for detecting or correcting errors.
Redundancy is added at the sender side and removed at the receiver side.
In general, the sender adds redundant bits through a process that creates a relation between redundant bits and actual data bits.
Redundancy is obtained using various coding schemes, where coding schemes can be divided into: Block coding and Convolutional coding.

## Slide 4: Block Coding
Divide the message into k-bits blocks, each called a dataword.
Add r redundant bits to each block to make the length .
The resulting n-bits blocks are called codewords.
Datawords of size k  datawords combinations are possible.
Codewords of size n  codewords combinations are possible.
Since n > k, hence number of possible codewords is greater than number of possible datawords.

## Slide 5: Block Coding (Cont.)
Block coding process is one-to-one (i.e. the same dataword is always encoded with the same codeword).
Hence, codewords are not used (called invalid codewords).
The error detection process is to detect the invalid codewords.
While using block codes, errors can be detected by receiver if:
  Receiver has a list of valid codewords.
  The original codeword has changed to an invalid codeword.

## Slide 6: Block Coding (Cont.)
Example: A coding scheme in which k = 4 and n = 5. We will have 2k = 16 datawords and 2n = 32 codewords, where 16 out of 32 codewords are used for message transfer and the rest will be considered as invalid.

## Slide 7: Error Detection in Block Coding
At the receiver side:
If received codeword is the same as one of the valid codewords, the codeword is accepted  corresponding dataword is extracted.
If received codeword is not valid, it is discarded.
If received codewrod is corrupted but still matches a valid codeword, the “error remains undetected”.
An error-detection code can detect only the types of errors for which it is designed; while other types of errors may remain undetected.

## Slide 8: Error Detection in Block Coding (Cont.)
Example: assume k = 2 and n = 3. Table below shows the list of datawords and codewords.

## Slide 9: Error Detection in Block Coding (Cont.)
Example: assume that sender encodes the dataword 01 as 011 and sends it to the receiver. Consider the following cases:
Receiver receives 011, i.e. a valid codeword. The receiver extracts the dataword 01 from it.
The codeword is corrupted and 111 is received, i.e. not a valid codeword. Hence, it is discarded.
Codeword is corrupted and 000 is received, i.e. a valid codeword. Hence, receiver incorrectly extracts dataword 00. Hence, two corrupted bits made error undetectable.

## Slide 10: Hamming Distance
Hamming distance: number of difference between corresponding bits of two words of same size, represented as .
Hamming distance between received codeword and sent codeword is the number of bits that got corrupted.
Example:
If Hamming distance between send and received codeword is not zero, the codeword has been corrupted.

## Slide 11: Hamming Distance (Cont.)
Apply XOR and count number of 1s.
Proper solution for programming in computers.

## Slide 12: Minimum Hamming Distance
Minimum Hamming distance: the smallest Hamming distance between all possible pairs of codewords in a set of codewords.
To guarantee the detection of up to errors in all cases, the minimum Hamming distance in a block of valid codewords must be .
Example: a code scheme has a minimum Hamming distance dmin = 4. What is the error detection capability of this scheme?
Solution: This code guarantees the detection of up to three errors, since dmin = s + 1  s = 3.

## Slide 13: Linear Block Code
Liner block code: a code in which XOR of two valid codewords creates another valid codeword.
Example: (previous example of k = 2 and n = 3, table given below).
In linear block codes, minimum Hamming distance is the number of 1s in nonzero valid codewords having the smallest number of 1s.

## Slide 14: Parity Check Code
In parity check code, a linear block code is used for error detection.
k-bit dataword is changed to n-bit codeword, where .
The extra bit is called parity bit, which is to make the total number of 1s in the codeword even or odd (Note: we will concentrate on even parity).
In parity check, , hence it’s single-bit error-detection code.
Example: (previous example of k = 2 and n = 3).

## Slide 15: Parity Check Code (Cont.)
Example: (k = 4 and n = 5), for Even parity.
Simple parity-check
code C(5, 4)

## Slide 16: Parity Check Code (Cont.)
Encoder and decoder for simple parity-check code C(5, 4)

## Slide 17: Parity Check Code (Cont.)
Example: for C(5, 4), at sender side the parity bit is generated using the four bits dataword ().
At receiver, the generated result is called syndrome
If syndrome is 0, there is no detectable error and data portion of received codeword is accepted as the dataword.
If syndrome is 1, data portion of received codeword is discarded.

## Slide 18: Parity Check Code (Cont.)
Example: Assume the sender sends the dataword 1011. The codeword created from this dataword is 10111, which is sent to the receiver. We examine five cases:
No error occurs; the received codeword is 10111. The syndrome is 0. The dataword 1011 is created.
One single-bit error changes a1 . The received codeword is 10011. The syndrome is 1. No dataword is created.
One single-bit error changes r0 . The received codeword is 10110. The syndrome is 1. No dataword is created.

## Slide 19: Parity Check Code (Cont.)
An error changes r0 and a second error changes a3 . The received codeword is 00110. The syndrome is 0. The dataword 0011 is created at the receiver. Note that here the dataword is wrongly created due to the syndrome value.
Three bits (a3, a2, and a1) are changed by errors. The received codeword is 01011, and the syndrome is 1. Hence, the dataword is not created.
Note: the above example shows that the simple parity check, guaranteed to detect one single error, can also find any odd number of errors.

## Slide 20: Two-dimensional Parity Check
The datawords are organized in a table (rows and columns).
Example:
Four datawords each of 7-bits are put in separate rows.
For each row and each column, 1 parity-check bit is calculated.

## Slide 21: Two-dimensional Parity Check (Cont.)
Example (Cont.):
The whole table is then sent to the receiver, which finds the syndrome for each row and each column.
The two-dimensional parity check can detect up to three errors that occur anywhere in the table. However, errors affecting 4 bits may not be detected.

## Slide 24: Cyclic Codes
Cyclic codes are special linear block codes with an extra property.
In cyclic code, if a code is cyclically shifted (i.e. rotated), the result is another codeword.
Example: if 1011000 is a codeword, then cyclically left-shifted will become 0110001 is also a codeword.
Cyclic redundancy check (CRC) is a cyclic code used in LANs and WANs for detecting errors.

## Slide 25: Cyclic Redundancy Check
Both linear and cyclic properties are observed in the table.
A CRC code with C(7, 4)

## Slide 26: Cyclic Redundancy Check (Cont.)
CRC encoder and decoder

## Slide 27: CRC (Cont.)
In example, k = 4, n = 7.
Number of 0s to add (n – k = 3).
Predefined and agreed upon divisor is of size (n – k + 1).
Apply modulu-2 division.
Multiply is AND operator.
Subtract is XOR operator.
Quotient is discarded, while
remainder is appended.

## Slide 28
Division in the CRC decoder for two cases
1

## Slide 29: CRC using Polynomials
Polynomial representation
A polynomial can also be like this:

## Slide 30: CRC using Polynomials (Cont.)
Things to remember before using polynomials:
Degree of polynomial is the highest power.
Add/subtract polynomial means to combine different terms, while deleting identical terms (only in pairs).
Multiply/divide polynomial means to add and subtract powers, respectively.
Multiply two polynomials is done term by term, followed by simplification.

## Slide 31: CRC using Polynomials (Cont.)
Divide one polynomial by another is done by dividing first term of dividend by first term of divisor to get first term of quotient, and so on. Repeat till dividend degree is less than divisor degree.
Shift binary patterns, where is number of shifted bits.
  Shift to the left:
    Adding extra 0s as rightmost bits.
    Multiply each polynomial term by .
Example:
  Shift left 3 bits, 10011  10011000, becomes .

## Slide 32
CRC division using polynomials

## Slide 33: Thank You!