## Slide 1: Assembly program for Embedded System
Dept. of Software Engineering
Bahria University, Karachi Campus
Embedded Systems: Using Assembly and C

## Slide 2
LOOP AND JUMP INSTRUCTIONS
Looping
Repeating a sequence of instructions a certain number of times is called a loop
  Loop action is performed by
DJNZ reg, Label
    The register is decremented
    If it is not zero, it jumps to the target address
referred to by the label
Prior to the start of loop the register is loaded with the counter for the number of repetitions
Counter can be R0 – R7 or RAM location
;This program adds value 3 to the ACC ten times
MOV MOV AGAIN: ADD
A,#0 R2,#10 A,#03
;A=0, clear ACC
;load counter R2=10
;add 03 to ACC
DJNZ R2,AGAIN ;repeat until R2=0,10 times MOV R5,A ;save A in R5
A loop can be repeated a
maximum of 255 times, if
R2 is FFH

## Slide 3
LOOP AND JUMP INSTRUCTIONS
Nested Loop
If we want to repeat an action more times than 256, we use a loop inside a loop, which is called nested loop
  We use multiple registers to hold the count
Write a program to (a) load the accumulator with the value 55H, and
(b) complement the ACC 700 times
 | MOV | A,#55H | ;A=55H | 
 | MOV | R3,#10 | ;R3=10, outer | loop count
NEXT: | MOV | R2,#70 | ;R2=70, inner | loop count
AGAIN: | CPL | A | ;complement A | register
DJNZ R2,AGAIN ;repeat it 70 times DJNZ R3,NEXT

## Slide 4
LOOP AND JUMP INSTRUCTIONS
Conditional Jumps
;A=R0
;jump if A = 0
;A=R1
;jump if A = 0
MOV A,R0
JZ OVER
MOV A,R1
JZ OVER
...
OVER:
Jump only if a certain condition is met
JZ label ;jump if A=0
Determine if R5 contains the value 0. If so, put 55H in it. |  |  | 
MOV | A,R5 | ;copy R5 to A | 
JNZ | NEXT | ;jump if A is not zero | 
MOV | R5,#55H |  | 
NEXT: ... |  |  | 
Can be used only for register A,
not any other register

## Slide 5: LOOP AND JUMP INSTRUCTIONS
Conditional Jumps (cont’)
All conditional jumps are short jumps
  The address of the target must within
-128 to +127 bytes of the contents of PC
Instructions | Actions
JZ | Jump if A ＝ 0
JNZ | Jump if A ≠ 0
DJNZ | Decrement and Jump if A ≠ 0
CJNE A,byte | Jump if A ≠ byte
CJNE reg,#data | Jump if byte ≠ #data
JC | Jump if CY ＝ 1
JNC | Jump if CY ＝ 0
JB | Jump if bit ＝ 1
JNB | Jump if bit ＝ 0
JBC | Jump if bit ＝ 1 and clear bit
8051 conditional jump instructions

## Slide 6
LOOP AND JUMP INSTRUCTIONS
Unconditional Jumps
The unconditional jump is a jump in which control is transferred unconditionally to the target location
LJMP (long jump)
  3-byte instruction
    First byte is the opcode
    Second and third bytes represent the 16-bit target address
      Any memory location from 0000 to FFFFH
SJMP (short jump)
  2-byte instruction
    First byte is the opcode
    Second byte is the relative target address
      00 to FFH (forward +127 and backward
-128 bytes from the current PC)

## Slide 7
LOOP AND JUMP INSTRUCTIONS
Calculating Short Jump Address
To calculate the target address of a short jump (SJMP, JNC, JZ, DJNZ, etc.)
  The second byte is added to the PC of the instruction immediately below the jump
If the target address is more than -128 to +127 bytes from the address below the short jump instruction
  The assembler will generate an error stating the jump is out of range

## Slide 8
CALL INSTRUCTIONS
LCALL
(cont’)
BACK:
ORG 0
MOV A,#55H
MOV P1,A
LCALL DELAY
MOV A,#0AAH
MOV P1,A
;load A with 55H
;send 55H to port 1
;time delay
;load A with AA (in hex)
;send AAH to port 1
LCALL DELAY SJMP BACK
;keep doing this indefinitely
;---------- this is delay subroutine ------------
300H R5,#0FFH R5,AGAIN
;put DELAY at address 300H
;R5=255 (FF in hex), counter
;stay here until R5 become 0
;return to caller (when R5 =0)
ORG DELAY: MOV AGAIN: DJNZ
RET END
;end of asm file
Upon executing “LCALL DELAY”, the address of instruction below it, “MOV A,#0AAH” is pushed onto stack, and the 8051 starts to execute at 300H.
The counter R5 is set to FFH; so loop is repeated 255 times.
When R5 becomes 0, control falls to the
RET which pops the address from the stack into the PC and resumes executing the instructions after the CALL.
The amount of time delay depends on the frequency of the 8051

## Slide 9: CALL INSTRUCTIONS
ACALL
(cont’)
BACK:
ORG 0
MOV A,#55H
MOV P1,A
ACALL DELAY
;load A with 55H
;send 55H to port 1
;time delay
;complement reg A
;keep doing this indefinitely
CPL A
SJMP BACK
... END
;end of asm file
BACK:
ORG 0
MOV A,#55H
MOV P1,A
LCALL DELAY
MOV A,#0AAH
MOV P1,A
;load A with 55H
;send 55H to port 1
;time delay
;load A with AA (in hex)
;send AAH to port 1
LCALL DELAY
;keep doing this indefinitely
SJMP BACK
... END
;end of asm file
A rewritten program which is more efficiently

## Slide 10
TIME DELAY FOR VARIOUS 8051 CHIPS
CPU executing an instruction takes a certain number of clock cycles
  These are referred as to as machine cycles
The length of machine cycle depends on the frequency of the crystal oscillator connected to 8051
In original 8051, one machine cycle lasts 12 oscillator periods
Find the period of the machine cycle for 11.0592 MHz crystal frequency
Solution:
11.0592/12 = 921.6 kHz;
machine cycle is 1/921.6 kHz = 1.085μs

## Slide 11: TIME DELAY FOR VARIOUS 8051 CHIPS (cont’)
For 8051 system of 11.0592 MHz, find how long it takes to execute each instruction.
(a) MOV R3,#55 (b) DEC R3 (c) DJNZ R2 target
(d) LJMP (e) SJMP (f) NOP (g) MUL AB
Solution:
Machine cycles
Time to execute
(a)
(b)
(c)
(d)
(e)
(f)
(g)
1
1
2
2
2
1
4
1x1.085μs 1x1.085μs 2x1.085μs 2x1.085μs 2x1.085μs 1x1.085μs 4x1.085μs
＝ 1.085μs
＝ 1.085μs
＝ 2.17μs
＝ 2.17μs
＝ 2.17μs
＝ 1.085μs
＝ 4.34μs

## Slide 12: TIME DELAY FOR VARIOUS 8051 CHIPS
Delay Calculation
Find the size of the delay in following program, if the crystal frequency is 11.0592MHz.
MOV AGAIN: MOV
A,#55H P1,A
ACALL DELAY CPL A SJMP AGAIN
;---time delay------- DELAY: MOV R3,#200 HERE: DJNZ R3,HERE
RET
Solution:
DELAY: MOV R3,#200 HERE: DJNZ R3,HERE
RET
Machine cycle
1
2
2
Therefore, [(200x2)+1+2]x1.085μs ＝ 436.255μs.
A simple way to short jump to itself in order to keep the microcontroller busy HERE: SJMP HERE
We can use the following:
SJMP $

## Slide 13: TIME DELAY FOR VARIOUS 8051 CHIPS
Increasing Delay Using NOP
Find the size of the delay in following program, if the crystal frequency is 11.0592MHz.
Machine Cycle
DELAY: | MOV | R3,#250 | 1
HERE: | NOP |  | 1
 | NOP |  | 1
 | NOP |  | 1
 | NOP |  | 1
 | DJNZ | R3,HERE | 2
 | RET |  | 2
Solution:
The time delay inside HERE loop is
[250(1+1+1+1+2)]x1.085μs ＝ 1627.5μs.
Adding the two instructions outside loop we
have 1627.5μs + 3 x 1.085μs ＝ 1630.755μs

## Slide 14: TIME DELAY FOR VARIOUS 8051 CHIPS
Large Delay Using Nested Loop
Find the size of the delay in following program, if the crystal frequency is 11.0592MHz.
Machine Cycle
DELAY: | MOV | R2,#200 | 1
AGAIN: | MOV | R3,#250 | 1
HERE: | NOP |  | 1
 | NOP |  | 1
 | DJNZ | R3,HERE | 2
 | DJNZ | R2,AGAIN | 2
 | RET |  | 2
Solution:
For HERE loop, we have (4x250)x1.085μs＝1085μs. For AGAIN loop repeats HERE loop 200 times, so we have 200x1085μs＝217000μs. But “MOV
R3,#250” and “DJNZ R2,AGAIN” at the start and end of the AGAIN loop add (3x200x1.805)=651μs. As a result we have 217000+651=217651μs.
Notice in nested loop, as in all other time delay loops, the time is approximate since we have ignored the first and last instructions in the subroutine.

## Slide 15
Two factors can affect the accuracy of TIME DELAY the delay FOR VARIOUS 8051 CHIPS  Crystal frequency The duration of the clock period of the machine cycle is a function of this crystal frequency Delay Calculation for  8051 design Other 8051  The original machine cycle duration was set at 12 clocks Advances in both IC technology and CPU design in recent years have made the 1-clock machine cycle a common feature Clocks per machine cycle for various 8051 versions |  |  | 
 |  | Chip/Maker | Clocks per Machine Cycle
 |  | AT89C51 Atmel | 12
 |  | P89C54X2 Philips | 6
 |  | DS5000 Dallas Semi | 4
 |  | DS89C420/30/40/50 Dallas Semi | 1

## Slide 16: TIME DELAY FOR VARIOUS 8051 CHIPS
Delay Calculation for Other 8051 (cont’)
Find the period of the machine cycle (MC) for various versions of 8051, if XTAL=11.0592 MHz.
(a) AT89C51 (b) P89C54X2 (c) DS5000 (d) DS89C4x0
Solution:
(a) 11.0592MHz/12 = 921.6kHz;
MC is 1/921.6kHz = 1.085μs ＝ 1085ns
(b) | 11.0592MHz/6 = 1.8432MHz; | 
 | MC is 1/1.8432MHz = 0.5425μs | ＝ 542ns
(c) | 11.0592MHz/4 = 2.7648MHz ; | 
 | MC is 1/2.7648MHz = 0.36μs ＝ | 360ns
(d) | 11.0592MHz/1 = 11.0592MHz; | 
 | MC is 1/11.0592MHz = 0.0904μs | ＝ 90ns

## Slide 17: TIME DELAY FOR VARIOUS 8051 CHIPS
Delay Calculation for Other 8051 (cont’)
For an AT8051 and DSC89C4x0 system of 11.0592 MHz, find how long it takes to execute each instruction.
(a) MOV R3,#55 (b) DEC R3 (c) DJNZ R2 target
(d) LJMP (e) SJMP (f) NOP (g) MUL AB
Solution:
AT8051 DS89C4x0
(a) 1×1085ns ＝ 1085ns 2×90ns = 180ns (b) 1×1085ns ＝ 1085ns 1×90ns = 90ns (c) 2×1085ns ＝ 2170ns 4×90ns = 360ns (d) 2×1085ns ＝ 2170ns 3×90ns = 270ns (e) 2×1085ns ＝ 2170ns 3×90ns = 270ns (f) 1×1085ns ＝ 1085ns 1×90ns = 90ns (g) 4×1085ns ＝ 4340ns 9×90ns = 810ns
Instruction | 8051 | DSC89C4x0
MOV R3,#55 | 1 | 2
DEC R3 | 1 | 1
DJNZ R2 target | 2 | 4
LJMP | 2 | 3
SJMP | 2 | 3
NOP | 1 | 1
MUL AB | 4 | 9