## Slide 1: TIMERS in Embedded System
Dr. Qamaruddin

## Slide 2
PROGRAMMING TIMERS
The 8051 has two timers/counters, they can be used either as
  Timers to generate a time delay or as
  Event counters to count events happening outside the microcontroller
Both Timer 0 and Timer 1 are 16 bits wide
  Since 8051 has an 8-bit architecture, each 16-bits timer is accessed as two separate registers of low byte and high byte

## Slide 3
PROGRAMMING TIMERS
Timer 0 & 1 Registers
Accessed as low byte and high byte
  The low byte register is called TL0/TL1 and
  The high byte register is called TH0/TH1
  Accessed like any other register
    MOV TL0,#4FH
    MOV R5,TH0
TH0 TL0
D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
TH1
TL1
D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0

## Slide 4
PROGRAMMING TIMERS
TMOD
Register
GATE | C/T | M1 | M0
Timer1 |  |  | 
GATE | C/T | M1 | M0
Timer0 |  |  | 
Both timers 0 and 1 use the same register, called TMOD (timer mode), to set the various timer operation modes
TMOD is a 8-bit register
  The lower 4 bits are for Timer 0
  The upper 4 bits are for Timer 1
  In each case,
    The lower 2 bits are used to set the timer mode
    The upper 2 bits to specify the operation
(MSB) (LSB)

## Slide 5
PROGRAMMING TIMERS
TMOD
Register
(cont’)
0 | 0 | 0 | 13-bit timer mode 8-bit timer/counter THx with TLx as 5-bit
 |  |  | prescaler
0 | 1 | 1 | 16-bit timer mode 16-bit timer/counter THx and TLx are
 |  |  | cascaded; there is no prescaler
1 | 0 | 2 | 8-bit auto reload 8-bit auto reload timer/counter; THx holds a
 |  |  | value which is to be reloaded TLx each time
 |  |  | it overfolws
1 | 1 | 3 | Split timer mode
Operating Mode
Mode
M1 M0
GATE
C/T M1
Timer1
M0
(MSB)
GATE
C/T M1
Timer0
M0
(LSB)
Timer or counter selected
Cleared for timer operation (input from internal system clock)
Set for counter operation (input from Tx input pin)
Gating control when set. Timer/counter is enable only while the INTx pin is high and the TRx control pin is set
When cleared, the timer is enabled whenever the TRx
control bit is set

## Slide 6
PROGRAMMING TIMERS
TMOD
Register
(cont’)
Example 9-1
Indicate which mode and which timer are selected for each of the following.
(a) MOV TMOD, #01H (b) MOV TMOD, #20H (c) MOV TMOD, #12H
Solution:
We convert the value from hex to binary. From Figure 9-3 we have:
TMOD = 00000001, mode 1 of timer 0 is selected.
TMOD = 00100000, mode 2 of timer 1 is selected.
TMOD = 00010010, mode 2 of timer 0, and mode 1 of timer 1 are selected.
Example 9-2
Find the timer’s clock frequency and its period for various 8051-based system, with the crystal frequency 11.0592 MHz when C/T bit of TMOD is 0.
Solution:
1/12  11.0529 MHz = 921.6 MHz; T = 1/921.6 kHz = 1.085 us
XTAL
oscillator
÷12
If C/T = 0, it is used as a timer for time delay generation.
The clock source for
the time delay is the crystal frequency of the 8051

## Slide 7
PROGRAMMING TIMERS
TMOD
Register
GATE
Timers of 8051 do starting and stopping by either software or hardware control
  In using software to start and stop the timer where GATE=0
    The start and stop of the timer are controlled by way of software by the TR (timer start) bits TR0 and TR1
      The SETB instruction starts it, and it is stopped by the CLR instruction
      These instructions start and stop the timers as long as GATE=0 in the TMOD register
  The hardware way of starting and stopping the timer by an external source is achieved
by making GATE=1 in the TMOD register
Find the value for TMOD if we want to program timer 0 in mode 2, use 8051 XTAL for the clock source, and use instructions to start and stop the timer.
TMOD = 0000 0010
Timer 0, mode 2
C/T = 0 to use XTAL clock source
gate = 0 to use
internal (software) start
and stop method.

## Slide 8
PROGRAMMING TIMERS
Mode 1 Programming
The following are the characteristics and operations of mode1:
  It is a 16-bit timer; therefore, it allows value of 0000 to FFFFH to be loaded into the timer’s register TL and TH
  After TH and TL are loaded with a 16-bit initial value, the timer must be started
    This is done by SETB TR0 for timer 0 and
SETB TR1 for timer 1
  After the timer is started, it starts to count up
    It counts up until it reaches its limit of FFFFH
XTAL
oscillator
TF
Overflow flag
TH
TL
÷12
TF goes high
when FFFF  0
TR
C/T = 0

## Slide 9
PROGRAMMING TIMERS
Mode 1 Programming (cont’)
(cont’)
  When it rolls over from FFFFH to 0000, it sets high a flag bit called TF (timer flag)
    Each timer has its own timer flag: TF0 for
timer 0, and TF1 for timer 1
    This timer flag can be monitored
  When this timer flag is raised, one option would be to stop the timer with the instructions CLR TR0 or CLR TR1, for timer 0 and timer 1, respectively
After the timer reaches its limit and rolls over, in order to repeat the process
  TH and TL must be reloaded with the original value, and
  TF must be reloaded to 0
XTAL
oscillator
TF
Overflow flag
TH
TL
÷12
TF goes high
when FFFF  0
TR
C/T = 0

## Slide 10
PROGRAMMING TIMERS
Mode 1 Programming
Steps to Mode 1 Program
To generate a time delay
Load the TMOD value register indicating which timer (timer 0 or timer 1) is to be used and which timer mode (0 or 1) is selected
Load registers TL and TH with initial count value
Start the timer
Keep monitoring the timer flag (TF) with the JNB TFx,target instruction to see if it is raised
  Get out of the loop when TF becomes high
Stop the timer
Clear the TF flag for the next round
Go back to Step 2 to load TH and TL again

## Slide 11: PROGRAMMING TIMERS
Mode 1 Programming
Steps to Mode 1 Program (cont’)
Example 9-4
In the following program, we create a square wave of 50% duty cycle (with equal portions high and low) on the P1.5 bit. Timer 0 is used to generate the time delay. Analyze the program
 | MOV | TMOD,#01 | ;Timer 0, | mode 1(16-bit | mode)
HERE: | MOV | TL0,#0F2H | ;TL0=F2H, | the low byte | 
 | MOV | TH0,#0FFH | ;TH0=FFH, | the high byte | 
CPL |  | P1.5 | ;toggle P1.5 |  | 
ACALL DELAY SJMP HERE
In the above program notice the following step.
TMOD is loaded.
FFF2H is loaded into TH0-TL0.
P1.5 is toggled for the high and low portions of the pulse.
…

## Slide 12
PROGRAMMING TIMERS
Mode 1 Programming
Steps to Mode 1 Program (cont’)
Example 9-4 (cont’)
DELAY:
SETB AGAIN: JNB | TR0 TF0,AGAIN | ;start the timer 0 ;monitor timer flag 0 ;until it rolls over
CLR | TR0 | ;stop timer 0
CLR | TF0 | ;clear timer 0 flag
RET |  | 
7. Timer 0 is stopped by the instruction CLR TR0. The DELAY subroutine ends, and the process is repeated.
Notice that to repeat the process, we must reload the TL and TH registers, and start the process is repeated …
The DELAY subroutine using the timer is called.
In the DELAY subroutine, timer 0 is started by the SETB TR0 instruction.
Timer 0 counts up with the passing of each clock, which is provided by the crystal oscillator. As the timer counts up, it goes through the states of FFF3, FFF4, FFF5, FFF6, FFF7, FFF8, FFF9, FFFA, FFFB, and so on until it
reaches FFFFH. One more clock rolls it to 0, raising the timer flag (TF0=1). At that point, the JNB instruction falls through.
FFF2 FFF3 FFF4 FFFF 0000
TF=0 TF=0 TF=0
TF=0 TF=1

## Slide 13
PROGRAMMING TIMERS
Mode 1 Programming
Steps to Mode 1 Program (cont’)
Example 9-5
In Example 9-4, calculate the amount of time delay in the DELAY subroutine generated by the timer. Assume XTAL = 11.0592 MHz.
Solution:
The timer works with a clock frequency of 1/12 of the XTAL frequency; therefore, we have 11.0592 MHz / 12 = 921.6 kHz as the timer frequency. As a result, each clock has a period of T = 1/921.6kHz = 1.085us. In other words, Timer 0 counts up each 1.085 us resulting in delay = number of counts  1.085us.
The number of counts for the roll over is FFFFH – FFF2H = 0DH (13 decimal). However, we add one to 13 because of the extra clock needed when it rolls over from FFFF to 0 and raise the TF flag. This gives 14  1.085us = 15.19us for half the pulse. For the entire period it is T = 2  15.19us = 30.38us as the time delay generated by the timer.
(a) in hex
(FFFF – YYXX + 1) 
1.085 us, where YYXX are TH, TL initial values respectively. Notice that value YYXX are in hex.
(b) in decimal Convert YYXX values of the TH, TL register to decimal to get a NNNNN decimal, then (65536 - NNNN) 
1.085 us

## Slide 14
PROGRAMMING TIMERS
Mode 1 Programming
Steps to Mode 1 Program (cont’)
Example 9-6
In Example 9-5, calculate the frequency of the square wave generated on pin P1.5.
Solution:
In the timer delay calculation of Example 9-5, we did not include the overhead due to instruction in the loop. To get a more accurate timing, we need to add clock cycles due to this instructions in the loop. To do that, we use the machine cycle from Table A-1 in Appendix A, as shown below.
Cycles
HERE: MOV
MOV
TL0,#0F2H TH0,#0FFH
CPL P1.5
ACALL DELAY SJMP HERE
DELAY:
SETB TR0
AGAIN: JNB TF0,AGAIN CLR TR0
CLR TF0
RET
2
2
1
2
2
1
14
1
1
2
Total 28
T = 2  28  1.085 us = 60.76 us and F = 16458.2 Hz

## Slide 15
PROGRAMMING TIMERS
Mode 1 Programming
Steps to Mode 1 Program (cont’)
Example 9-7
Find the delay generated by timer 0 in the following code, using both of the Methods of Figure 9-4. Do not include the overhead due to instruction.
HERE:
AGAIN:
CLR MOV MOV | P2.3 TMOD,#01 TL0,#3EH | ;Clear P2.3 ;Timer 0, 16-bitmode ;TL0=3Eh, the low byte
MOV SETB | TH0,#0B8H ;TH0=B8H, the high byte P2.3 ;SET high timer 0 | 
SETB | TR0 | ;Start the timer 0
JNB TF0,AGAIN ;Monitor timer flag 0 |  | 
CLR | TR0 | ;Stop the timer 0
CLR | TF0 | ;Clear TF0 for next round
CLR | P2.3 | 
Solution:
(a) (FFFFH – B83E + 1) = 47C2H = 18370 in decimal and 18370 
1.085 us = 19.93145 ms
(b) Since TH – TL = B83EH = 47166 (in decimal) we have 65536 – 47166 = 18370. This means that the timer counts from B38EH to FFFF. This plus Rolling over to 0 goes through a total of 18370 clock cycles, where each clock is 1.085 us in duration. Therefore, we have 18370  1.085 us = 19.93145 ms as the width of the pulse.

## Slide 16
PROGRAMMING TIMERS
Mode 1 Programming
Steps to Mode 1 Program (cont’)
Example 9-8
Modify TL and TH in Example 9-7 to get the largest time delay possible. Find the delay in ms. In your calculation, exclude the overhead due to the instructions in the loop.
Solution:
To get the largest delay we make TL and TH both 0. This will count up from 0000 to FFFFH and then roll over to zero.
TMOD,#01 ;Timer 0, 16-bitmode
HERE:
CLR P2.3 ;Clear P2.3 MOV
MOV
TL0,#0
MOV TH0,#0
SETB P2.3
;TL0=0, the low byte
;TH0=0, the high byte
;SET high P2.3
SETB TR0 ;Start timer 0
AGAIN: JNB TF0,AGAIN ;Monitor timer flag 0
CLR | TR0 | ;Stop the timer 0
CLR | TF0 | ;Clear timer 0 flag
CLR | P2.3 | 
Making TH and TL both zero means that the timer will count from 0000 to FFFF, and then roll over to raise the TF flag. As a result, it goes through a total Of 65536 states. Therefore, we have delay = (65536 - 0)  1.085 us = 71.1065ms.

## Slide 17
PROGRAMMING TIMERS
Mode 1 Programming
Steps to Mode 1 Program (cont’)
Example 9-9
The following program generates a square wave on P1.5 continuously using timer 1 for a time delay. Find the frequency of the square wave if XTAL = 11.0592 MHz. In your calculation do not include the overhead due to Instructions in the loop.
MOV AGAIN: MOV
TMOD,#10;Timer 1, mod 1 (16-bitmode) TL1,#34H ;TL1=34H, low byte of timer
MOV TH1,#76H ;TH1=76H, high byte timer
SETB TR1 ;start the timer 1
BACK:
JNB TF1,BACK ;till timer rolls over
CLR TR1 ;stop the timer 1
CPL | P1.5 | ;comp. p1. to get hi, lo
CLR | TF1 | ;clear timer flag 1
SJMP | AGAIN | ;is not auto-reload
Solution:
Since FFFFH – 7634H = 89CBH + 1 = 89CCH and 89CCH = 35276
clock count and 35276  1.085 us = 38.274 ms for half of the square wave. The frequency = 13.064Hz.
Also notice that the high portion and low portion of the square wave pulse are equal. In the above calculation, the overhead due to all the instruction in the loop is not included.

## Slide 18
PROGRAMMING TIMERS
Mode 1 Programming
Finding the Loaded Timer Values
To calculate the values to be loaded into the TL and TH registers, look at the following example
  Assume XTAL = 11.0592 MHz, we can use the following steps for finding the TH, TL registers’ values
    Divide the desired time delay by 1.085 us
    Perform 65536 – n, where n is the decimal value we got in Step1
    Convert the result of Step2 to hex, where yyxx is the initial hex value to be loaded into the timer’s register
    Set TL = xx and TH = yy

## Slide 19
PROGRAMMING TIMERS
Mode 1 Programming
Finding the Loaded Timer Values (cont’)
Example 9-10
Assume that XTAL = 11.0592 MHz. What value do we need to load the timer’s register if we want to have a time delay of 5 ms (milliseconds)? Show the program for timer 0 to create a pulse width of 5 ms on P2.3.
Solution:
Since XTAL = 11.0592 MHz, the counter counts up every 1.085 us. This means that out of many 1.085 us intervals we must make a 5 ms pulse. To get that, we divide one by the other. We need 5 ms / 1.085 us = 4608 clocks. To Achieve that we need to load into TL and TH the value 65536 – 4608 = EE00H. Therefore, we have TH = EE and TL = 00.
TMOD,#01 ;Timer 0, 16-bitmode
HERE:
CLR P2.3 ;Clear P2.3 MOV
MOV
TL0,#0 ;TL0=0, the low byte
MOV TH0,#0EEH ;TH0=EE, the high byte SETB P2.3 ;SET high P2.3
SETB TR0 ;Start timer 0
AGAIN: JNB TF0,AGAIN ;Monitor timer flag 0
CLR TR0
CLR TF0
;Stop the timer 0
;Clear timer 0 flag

## Slide 20
PROGRAMMING TIMERS
Mode 1 Programming
Finding the Loaded Timer Values (cont’)
Example 9-11
Assume that XTAL = 11.0592 MHz, write a program to generate a square wave of 2 kHz frequency on pin P1.5.
SJMP AGAIN
;Reload timer
Solution:
This is similar to Example 9-10, except that we must toggle the bit to generate the square wave. Look at the following steps.
T = 1 / f = 1 / 2 kHz = 500 us the period of square wave.
1 / 2 of it for the high and low portion of the pulse is 250 us.
250 us / 1.085 us = 230 and 65536 – 230 = 65306 which in hex is FF1AH.
TL = 1A and TH = FF, all in hex. The program is as follow.
MOV AGAIN: MOV
TMOD,#01 ;Timer 0, 16-bitmode TL1,#1AH ;TL1=1A, low byte of timer
MOV TH1,#0FFH ;TH1=FF, the high byte SETB TR1 ;Start timer 1
BACK:
JNB TF1,BACK ;until timer rolls over
CLR | TR1 | ;Stop the timer 1
CLR | P1.5 | ;Clear timer flag 1
CLR | TF1 | ;Clear timer 1 flag

## Slide 21
PROGRAMMING TIMERS
Mode 1 Programming
Finding the Loaded Timer Values (cont’)
Example 9-12
Assume XTAL = 11.0592 MHz, write a program to generate a square wave of 50 kHz frequency on pin P2.3.
Solution:
Look at the following steps.
T = 1 / 50 = 20 ms, the period of square wave.
1 / 2 of it for the high and low portion of the pulse is 10 ms.
10 ms / 1.085 us = 9216 and 65536 – 9216 = 56320 in decimal, and in hex it is DC00H.
TL = 00 and TH = DC (hex).
TMOD,#10H TL1,#00
;Timer 1, mod 1
;TL1=00,low byte of timer
MOV AGAIN: MOV
MOV
TH1,#0DCH ;TH1=DC, the high byte
SETB TR1
BACK: JNB
CLR CLR
TF1,BACK TR1
P2.3
SJMP AGAIN
;Start timer 1
;until timer rolls over
;Stop the timer 1
;Comp. p2.3 to get hi, lo
;Reload timer
;mode 1 isn’t auto-reload

## Slide 22: PROGRAMMING TIMERS
Mode 1 Programming
Generating Large Time Delay
Example 9-13
Examine the following program and find the time delay in seconds.
Exclude the overhead due to the instructions in the loop.
MOV TMOD,#10H ;Timer 1, mod 1
 | MOV | R3,#200 | ;cnter for multiple delay
AGAIN: | MOV | TL1,#08H | ;TL1=08,low byte of timer
 | MOV | TH1,#01H | ;TH1=01,high byte
 | SETB | TR1 | ;Start timer 1
BACK: | JNB | TF1,BACK | ;until timer rolls over
CLR |  | TR1 | ;Stop the timer 1
CLR |  | TF1 | ;clear Timer 1 flag
DJNZ |  | R3,AGAIN | ;if R3 not zero then ;reload timer
Solution:
TH-TL = 0108H = 264 in decimal and 65536 – 264 = 65272. Now
65272  1.085 s = 70.820 ms, and for 200 of them we have 200 70.820 ms = 14.164024 seconds.

## Slide 23
PROGRAMMING TIMERS
Mode 2 Programming
The following are the characteristics and operations of mode 2:
It is an 8-bit timer; therefore, it allows only values of 00 to FFH to be loaded into the timer’s register TH
After TH is loaded with the 8-bit value, the 8051 gives a copy of it to TL
Then the timer must be started
This is done by the instruction SETB TR0 for timer 0 and SETB TR1 for timer 1
After the timer is started, it starts to count up by incrementing the TL register
  It counts up until it reaches its limit of FFH
  When it rolls over from FFH to 00, it sets high the TF (timer flag)

## Slide 24: 4. When the TL register rolls from FFH to 0 and TF is set to 1, TL is reloaded automatically with the original value kept by the TH register
PROGRAMMING TIMERS
Mode 2 Programming (cont’)
To repeat the process, we must simply clear TF and let it go without any need by the programmer to reload the original value
This makes mode 2 an auto-reload, in contrast with mode 1 in which the programmer has to reload TH and TL
XTAL
oscillator
÷12
TR
TH
TL
C/T = 0
TF
TF goes high when FF  0
Overflow flag
Reload

## Slide 25
PROGRAMMING TIMERS
Mode 2 Programming
Steps to Mode 2 Program
To generate a time delay
Load the TMOD value register indicating which timer (timer 0 or timer 1) is to be used, and the timer mode (mode 2) is selected
Load the TH registers with the initial count value
Start timer
Keep monitoring the timer flag (TF) with the JNB TFx,target instruction to see whether it is raised
  Get out of the loop when TF goes high
Clear the TF flag
Go back to Step4, since mode 2 is auto- reload

## Slide 26: PROGRAMMING TIMERS
Mode 2 Programming
Steps to Mode 2 Program (cont’)
Example 9-14
Assume XTAL = 11.0592 MHz, find the frequency of the square wave generated on pin P1.0 in the following program
MOV MOV | TMOD,#20H TH1,#5 | ;T1/8-bit/auto reload ;TH1 = 5
SETB | TR1 | ;start the timer 1
BACK: JNB | TF1,BACK | ;till timer rolls over
CPL | P1.0 | ;P1.0 to hi, lo
CLR | TF1 | ;clear Timer 1 flag
SJMP | BACK | ;mode 2 is auto-reload
Solution:
First notice the target address of SJMP. In mode 2 we do not need to reload TH since it is auto-reload. Now (256 - 05)  1.085 us = 251  1.085 us = 272.33 us is the high portion of the pulse. Since it is a 50% duty cycle square wave, the period T is twice that; as a result T = 2  272.33 us = 544.67 us and the frequency = 1.83597 kHz

## Slide 27: PROGRAMMING TIMERS
Mode 2 Programming
Steps to Mode 2 Program (cont’)
Example 9-15
Find the frequency of a square wave generated on pin P1.0.
Solution:
MOV TMOD,#2H
;Timer 0, mod 2
;(8-bit, auto reload)
MOV AGAIN: MOV
TH0,#0 R5,#250
;multiple delay count
ACALL DELAY CPL P1.0
 | SJMP | AGAIN | 
DELAY: | SETB | TR0 | ;start the timer 0
BACK: | JNB | TF0,BACK | ;stay timer rolls over
 | CLR | TR0 | ;stop timer
 | CLR | TF0 | ;clear TF for next round
 | DJNZ | R5,DELAY | 
 | RET |  | 
T = 2 ( 250  256  1.085 us ) = 138.88ms, and frequency = 72 Hz

## Slide 28
PROGRAMMING TIMERS
Mode 2 Programming
Steps to Mode 2 Program (cont’)
Example 9-16
Assuming that we are programming the timers for mode 2, find the value (in hex) loaded into TH for each of the following cases.
(a)
(c)
(e)
MOV | TH1,#-200 | (b) | MOV | TH0,#-60
MOV | TH1,#-3 | (d) | MOV | TH1,#-12
MOV | TH0,#-48 |  |  | 
Solution:
You can use the Windows scientific calculator to verify the result provided by the assembler. In Windows calculator, select decimal and enter 200. Then select hex, then +/- to get the TH value. Remember that we only use the right two digits and ignore the rest since our data is an 8-bit data.
Decimal 2’s complement (TH value)
-3 FDH
-12 F4H
-48
-60
-200
D0H C4H 38H
The advantage of using negative values is that you don’t need to calculate the value loaded to THx
The number 200 is the timer count till the TF
is set to 1

## Slide 29
COUNTER PROGRAMMING
Timers can also be used as counters counting events happening outside the 8051
  When it is used as a counter, it is a pulse outside of the 8051 that increments the TH, TL registers
  TMOD and TH, TL registers are the same as for the timer discussed previously
Programming the timer in the last section also applies to programming it as a counter
  Except the source of the frequency

## Slide 30
COUNTER PROGRAMMING
C/T Bit in TMOD Register
Pin | Port Pin | Function Description
14 | P3.4 | T0 Timer/counter 0 external input
15 | P3.5 | T1 Timer/counter 1 external input
The C/T bit in the TMOD registers decides the source of the clock for the timer
  When C/T = 1, the timer is used as a counter and gets its pulses from outside the 8051
    The counter counts up as pulses are fed from pins 14 and 15, these pins are called T0 (timer 0 input) and T1 (timer 1 input)
Port 3 pins used for Timers 0 and 1

## Slide 31
COUNTER PROGRAMMING
C/T Bit in TMOD Register (cont’)
Example 9-18
Assuming that clock pulses are fed into pin T1, write a program for counter 1 in mode 2 to count the pulses and display the state of the TL1 count on P2, which connects to 8 LEDs.
TM0D,#01100000B ;counter 1, mode 2,
;C/T=1 external pulses
TH1,#0 P3.5 TR1 A,TL1
;clear TH1
;make T1 input
;start the counter
;get copy of TL
P2,A ;display it on port 2
TF1,Back ;keep doing, if TF = 0
Solution:
MOV
MOV SETB
AGAIN: SETB
BACK: MOV
MOV JNB CLR CLR SJMP
TR1 ;stop the counter 1 TF1 ;make TF=0
AGAIN ;keep doing it
Notice in the above program the role of the instruction SETB P3.5.
Since ports are set up for output when the 8051 is powered up, we make P3.5 an input port by making it high. In other words, we must configure (set high) the T1 pin (pin P3.5) to allow pulses to be fed into it.

## Slide 32: COUNTER PROGRAMMING
C/T Bit in TMOD Register (cont’)
TR
TH TL
TF
TF goes high when FFFF  0
Overflow flag
Timer external input pin
3.4 or 3.5
C/T = 1
TR
TH
TL
TF
TF goes high when FF  0
Overflow flag
Reload
Timer external input pin
3.4 or 3.5
C/T = 1
Timer with external input (Mode 1)
Timer with external input (Mode 2)

## Slide 33
COUNTER PROGRAMMING
TCON
Register
TCON (timer control) register is an 8- bit register
TCON: Timer/Counter Control Register
TF1 | TR1 | TF0 | TR0 | IE1 | IT1 | IE0 | IT0
The upper four bits are used to store the TF and TR bits of both timer 0 and 1
The lower 4 bits are set aside for controlling the interrupt bits

## Slide 34
COUNTER PROGRAMMING
TCON
Register
(cont’)
For timer 0
SETB TR0 = SETB TCON.4
CLR TR0 = CLR TCON.4
SETB TF0 = SETB TCON.5
CLR TF0 = CLR TCON.5
For timer 1
SETB TR1 = SETB TCON.6
CLR TR1 = CLR TCON.6
SETB TF1 = SETB TCON.7
CLR TF1 = CLR TCON.7
TCON register is a bit-addressable register
Equivalent instruction for the Timer Control Register

## Slide 35
COUNTER PROGRAMMING
TCON
Register
Case of GATE = 1
If GATE = 1, the start and stop of the timer are done externally through pins P3.2 and P3.3 for timers 0 and 1, respectively
  This hardware way allows to start or stop the timer externally at any time via a simple switch
XTAL
oscillator
÷12
TR
C/T = 0
Gate INT0 Pin
Pin 3.2 or 3.3
C/T = 1
Tx Pin Pin 3.4 or 3.5

## Slide 36: PROGRAMMING TIMERS IN C
Accessing Timer Registers
Example 9-20
Write an 8051 C program to toggle all the bits of port P1 continuously with some delay in between. Use Timer 0, 16-bit mode to generate the delay.
Solution:
#include <reg51.h> void T0Delay(void); void main(void){
while (1) {
P1=0x55;
T0Delay(); P1=0xAA;
T0Delay();
}
}
void T0Delay(){ TMOD=0x01; TL0=0x00; TH0=0x35; TR0=1;
while (TF0==0);
TR0=0; TF0=0;
}
FFFFH – 3500H = CAFFH
= 51967 + 1 = 51968
51968  1.085 s = 56.384 ms is the approximate delay

## Slide 37
PROGRAMMING TIMERS IN C
Calculating Delay Length Using Timers
To speed up the 8051, many recent versions of the 8051 have reduced the number of clocks per machine cycle from 12 to four, or even one
The frequency for the timer is always 1/12th the frequency of the crystal attached to the 8051, regardless of the 8051 version

## Slide 38: PROGRAMMING TIMERS IN C
Times 0/1 Delay Using Mode 1 (16-bit Non Auto- reload)
Example 9-21
Write an 8051 C program to toggle only bit P1.5 continuously every 50 ms. Use Timer 0, mode 1 (16-bit) to create the delay. Test the program on the (a) AT89C51 and (b) DS89C420.
Solution:
#include <reg51.h> void T0M1Delay(void); sbit mybit=P1^5;
void main(void){
while (1) { mybit=~mybit; T0M1Delay();
}
}
void T0M1Delay(void){ TMOD=0x01; TL0=0xFD;
TH0=0x4B; TR0=1;
while (TF0==0); TR0=0;
TF0=0;
}
FFFFH – 4BFDH = B402H
= 46082 + 1 = 46083
46083  1.085 s = 50 ms

## Slide 39: PROGRAMMING TIMERS IN C
Times 0/1 Delay Using Mode 1 (16-bit Non Auto- reload)
(cont’)
Example 9-22
Write an 8051 C program to toggle all bits of P2 continuously every 500 ms. Use Timer 1, mode 1 to create the delay.
Solution:
//tested for DS89C420, XTAL = 11.0592 MHz
#include <reg51.h> void T1M1Delay(void); void main(void){
unsigned char x;
P2=0x55;
while (1) { P2=~P2;
for (x=0;x<20;x++)
T1M1Delay();
}
}
void T1M1Delay(void){ TMOD=0x10; TL1=0xFE;
TH1=0xA5; TR1=1;
while (TF1==0); TR1=0;
TF1=0;
}
A5FEH = 42494 in decimal 65536 – 42494 = 23042
23042  1.085 s = 25 ms and
20  25 ms = 500 ms

## Slide 40: PROGRAMMING TIMERS IN C
Times 0/1 Delay Using Mode 1 (16-bit Non Auto- reload)
(cont’)
Example 9-25
A switch is connected to pin P1.2. Write an 8051 C program to monitor SW and create the following frequencies on pin P1.7: SW=0: 500Hz
SW=1: 750Hz, use Timer 0, mode 1 for both of them.
Solution:
#include <reg51.h> sbit mybit=P1^5; sbit SW=P1^7;
void T0M1Delay(unsigned char);
void main(void){ SW=1;
while (1) { mybit=~mybit; if (SW==0)
T0M1Delay(0);
else
T0M1Delay(1);
}
}
.....

## Slide 41: PROGRAMMING TIMERS IN C
Times 0/1 Delay Using Mode 1 (16-bit Non Auto- reload)
(cont’)
Example 9-25
.....
void T0M1Delay(unsigned char c){ TMOD=0x01;
if (c==0) {
TL0=0x67; TH0=0xFC;
}
else {
TL0=0x9A; TH0=0xFD;
} TR0=1;
while (TF0==0); TR0=0;
TF0=0;
}
FC67H = 64615
65536 – 64615 = 921
921  1.085 s = 999.285 s
1 / (999.285 s  2) = 500 Hz

## Slide 42: PROGRAMMING TIMERS IN C
Times 0/1 Delay Using Mode 2 (8-bit Auto-reload)
Example 9-23
Write an 8051 C program to toggle only pin P1.5 continuously every 250 ms. Use Timer 0, mode 2 (8-bit auto-reload) to create the delay.
Solution:
#include <reg51.h> void T0M2Delay(void); sbit mybit=P1^5;
void main(void){
unsigned char x,y; while (1) {
mybit=~mybit;
for (x=0;x<250;x++)
for (y=0;y<36;y++) //we put 36, not 40 T0M2Delay();
}
}
void T0M2Delay(void){ TMOD=0x02;
TH0=-23; TR0=1;
while (TF0==0); TR0=0;
TF0=0;
}
256 – 23 = 233
23  1.085 s = 25 s and
25 s  250  40 = 250 ms
Due to overhead of the for loop in C, we put 36 instead of 40

## Slide 43: PROGRAMMING TIMERS IN C
Times 0/1 Delay Using Mode 2 (8-bit Auto-reload) (cont’)
Example 9-24
Write an 8051 C program to create a frequency of 2500 Hz on pin P2.7. Use Timer 1, mode 2 to create delay.
Solution:
#include <reg51.h> void T1M2Delay(void); sbit mybit=P2^7;
void main(void){ unsigned char x; while (1) {
mybit=~mybit;
T1M2Delay();
}
}
void T1M2Delay(void){ TMOD=0x20;
TH1=-184;
TR1=1;
while (TF1==0); TR1=0;
TF1=0;
}
1/2500 Hz = 400 s
400 s /2 = 200 s
200 s / 1.085 s = 184