## Slide 1: PROGRAMMING IN C
Department of Software Engineering
Bahria University, Karachi Campus
Dr. Qamaruddin

## Slide 2
WHY PROGRAM 8051 IN C
Compilers produce hex files that is downloaded to ROM of microcontroller
  The size of hex file is the main concern
    Microcontrollers have limited on-chip ROM
    Code space for 8051 is limited to 64K bytes
C programming is less time consuming, but has larger hex file size
The reasons for writing programs in C
  It is easier and less time consuming to write in C than Assembly
  C is easier to modify and update
  You can use code available in function libraries
  C code is portable to other microcontroller with little of no modification

## Slide 3
DATA TYPES
A good understanding of C data types for 8051 can help programmers to create smaller hex files
  Unsigned char
  Signed char
  Unsigned int
  Signed int
  Sbit (single bit)
  Bit and sfr

## Slide 4
DATA TYPES
Unsigned char
The character data type is the most natural choice
  8051 is an 8-bit microcontroller
Unsigned char is an 8-bit data type in the range of 0 – 255 (00 – FFH)
  One of the most widely used data types for the 8051
    Counter value
    ASCII characters
C compilers use the signed char as the default if we do not put the keyword unsigned

## Slide 5: DATA TYPES
Unsigned char
(cont’)
Write an 8051 C program to send values 00 – FF to port P1.
Solution:
#include <reg51.h> void main(void)
{
unsigned char z;
for (z=0;z<=255;z++) P1=z;
}
Write an 8051 C program to send hex values for ASCII characters of 0, 1, 2, 3, 4, 5, A, B, C, and D to port P1.
Solution:
#include <reg51.h> void main(void)
{
unsigned char mynum[]=“012345ABCD”; unsigned char z;
for (z=0;z<=10;z++) P1=mynum[z];
}
Pay careful attention to the size of the data
Try to use unsigned char
instead of int if possible

## Slide 6: DATA TYPES
Unsigned char
(cont’)
Write an 8051 C program to toggle all the bits of P1 continuously.
Solution:
//Toggle P1 forever #include <reg51.h> void main(void)
{
for (;;)
{
p1=0x55; p1=0xAA;
}
}

## Slide 7
DATA TYPES
Signed char
The signed char is an 8-bit data type
  Use the MSB D7 to represent – or +
  Give us values from –128 to +127
We should stick with the unsigned char unless the data needs to be represented as signed numbers
  temperature
Write an 8051 C program to send values of –4 to +4 to port P1.
Solution:
//Singed numbers #include <reg51.h> void main(void)
{
char mynum[]={+1,-1,+2,-2,+3,-3,+4,-4};
unsigned char z; for (z=0;z<=8;z++)
P1=mynum[z];
}

## Slide 8
DATA TYPES
Unsigned and Signed int
The unsigned int is a 16-bit data type
  Takes a value in the range of 0 to 65535 (0000 – FFFFH)
  Define 16-bit variables such as memory addresses
  Set counter values of more than 256
  Since registers and memory accesses are in 8-bit chunks, the misuse of int variables will result in a larger hex file
Signed int is a 16-bit data type
  Use the MSB D15 to represent – or +
  We have 15 bits for the magnitude of the number from –32768 to +32767

## Slide 9: DATA TYPES
Single Bit
(cont’)
Write an 8051 C program to toggle bit D0 of the port P1 (P1.0) 50,000 times.
Solution:
#include <reg51.h> sbit MYBIT=P1^0;
void main(void)
{
unsigned int z;
for (z=0;z<=50000;z++)
{
MYBIT=0; MYBIT=1;
}
}
sbit keyword allows access to the single bits of the SFR registers

## Slide 10
DATA TYPES
Bit and sfr
The bit data type allows access to single bits of bit-addressable memory spaces 20 – 2FH
To access the byte-size SFR registers, we use the sfr data type
Data Type | Size in Bits | Data Range/Usage
unsigned char | 8-bit | 0 to 255
(signed) char | 8-bit | -128 to +127
unsigned int | 16-bit | 0 to 65535
(signed) int | 16-bit | -32768 to +32767
sbit | 1-bit | SFR bit-addressable only
bit | 1-bit | RAM bit-addressable only
sfr | 8-bit | RAM addresses 80 – FFH only

## Slide 11
TIME DELAY
There are two way s to create a time delay in 8051 C
  Using the 8051 timer
    The crystal frequency connected to the X1 – X2 input pins
  Using a simple for loop
    Compiler choice
      C compiler converts the C statements and functions to Assembly language instructions
      Different compilers produce different code

## Slide 12
TIME DELAY
(cont’)
Write an 8051 C program to toggle bits of P1 continuously forever with some delay.
Solution:
//Toggle P1 forever with some delay in between
//“on” and “off” #include <reg51.h> void main(void)
{
unsigned int x;
for (;;) //repeat forever
{
p1=0x55;
for (x=0;x<40000;x++); //delay size
//unknown
p1=0xAA;
for (x=0;x<40000;x++);
}
}
We must use the oscilloscope to measure the exact duration

## Slide 13
TIME DELAY
(cont’)
Write an 8051 C program to toggle bits of P1 ports continuously with a 250 ms.
Solution:
#include <reg51.h>
void MSDelay(unsigned int); void main(void)
{
//repeat forever
while (1)
{
p1=0x55;
MSDelay(250); p1=0xAA;
MSDelay(250);
}
}
void MSDelay(unsigned int itime)
{
unsigned int i,j;
for (i=0;i<itime;i++) for (j=0;j<1275;j++);
}

## Slide 14: I/O PROGRAMMING
Byte Size I/O
LEDs are connected to bits P1 and P2. Write an 8051 C program that shows the count from 0 to FFH (0000 0000 to 1111 1111 in binary) on the LEDs.
Solution:
#include <reg51.h> #defind LED P2;
//clear P1
//clear P2
//repeat forever
//increment P1
//increment P2
void main(void)
{
P1=00; LED=0;
for (;;)
{
P1++; LED++;
}
}
Ports P0 – P3 are byte-accessable and we use the P0 – P3 labels as defined in the 8051/52 header file.

## Slide 15: I/O PROGRAMMING
Byte Size I/O
(cont’)
Write an 8051 C program to get a byte of data form P1, wait 1/2 second, and then send it to P2.
Solution:
#include <reg51.h>
void MSDelay(unsigned int);
//make P1 input port
//get a byte from P1
//send it to P2
void main(void)
{
unsigned char mybyte; P1=0xFF;
while (1)
{
mybyte=P1; MSDelay(500); P2=mybyte;
}
}

## Slide 16: I/O PROGRAMMING
Byte Size I/O
(cont’)
Write an 8051 C program to get a byte of data form P0. If it is less than 100, send it to P1; otherwise, send it to P2.
Solution:
#include <reg51.h>
//make P0 input port
//get a byte from P0
//send it to P1
//send it to P2
void main(void)
{
unsigned char mybyte; P0=0xFF;
while (1)
{
mybyte=P0;
if (mybyte<100) P1=mybyte;
else
P2=mybyte;
}
}

## Slide 17: I/O PROGRAMMING
Bit-addressable I/O
Write an 8051 C program to toggle only bit P2.4 continuously without disturbing the rest of the bits of P2.
Solution:
//Toggling an individual bit #include <reg51.h>
sbit mybit=P2^4;
//turn on P2.4
//turn off P2.4
void main(void)
{
while (1)
{
mybit=1; mybit=0;
}
}
Ports P0 – P3 are bit- addressable and we use sbit data type to access a single bit of P0 - P3
Use the Px^y format, where x is the port 0, 1, 2, or 3 and y is the bit 0 – 7 of that port

## Slide 18: I/O PROGRAMMING
Bit-addressable I/O
(cont’)
Write an 8051 C program to monitor bit P1.5. If it is high, send 55H to P0; otherwise, send AAH to P2.
Solution:
#include <reg51.h> sbit mybit=P1^5;
//make mybit an input
void main(void)
{
mybit=1; while (1)
{
if (mybit==1) P0=0x55;
else
P2=0xAA;
}
}

## Slide 19: I/O PROGRAMMING
Bit-addressable I/O
(cont’)
A door sensor is connected to the P1.1 pin, and a buzzer is connected to P1.7. Write an 8051 C program to monitor the door sensor, and when it opens, sound the buzzer. You can sound the buzzer by sending a square wave of a few hundred Hz.
Solution:
#include <reg51.h>
void MSDelay(unsigned int); sbit Dsensor=P1^1;
sbit Buzzer=P1^7;
void main(void)
{
}
}
Dsensor=1; //make P1.1 an input while (1)
{
while (Dsensor==1)//while it opens
{
Buzzer=0; MSDelay(200); Buzzer=1; MSDelay(200);
}

## Slide 20: I/O PROGRAMMING
Bit-addressable I/O
(cont’)
The data pins of an LCD are connected to P1. The information is latched into the LCD whenever its Enable pin goes from high to low. Write an 8051 C program to send “The Earth is but One Country” to this LCD.
Solution:
#include <reg51.h>
}
}
#define LCDData P1 sbit En=P2^0;
//LCDData declaration
//the enable pin
void main(void)
{
unsigned char message[]
=“The Earth is but One Country”; unsigned char z;
for (z=0;z<28;z++) //send 28 characters
{
LCDData=message[z];
En=1; En=0;
//a high-
//-to-low pulse to latch data

## Slide 21: I/O PROGRAMMING
Accessing SFR Addresses 80 - FFH
Write an 8051 C program to toggle all the bits of P0, P1, and P2 continuously with a 250 ms delay. Use the sfr keyword to declare the port addresses.
Solution:
//Accessing Ports as SFRs using sfr data type sfr P0=0x80;
sfr P1=0x90; sfr P2=0xA0;
void MSDelay(unsigned int);
void main(void)
{
while (1)
{
P0=0x55; P1=0x55; P2=0x55;
MSDelay(250);
P0=0xAA; P1=0xAA; P2=0xAA;
MSDelay(250);
}
}
Another way to access the SFR RAM space 80 – FFH is to use the sfr data type

## Slide 22: I/O PROGRAMMING
Accessing SFR Addresses 80 - FFH
(cont’)
Write an 8051 C program to turn bit P1.5 on and off 50,000 times.
Solution:
sbit MYBIT=0x95;
void main(void)
{
unsigned int z;
for (z=0;z<50000;z++)
{
MYBIT=1; MYBIT=0;
}
}
We can access a single bit of any SFR if we specify the bit address
Notice that there is no #include <reg51.h>. This allows us to access any byte of the SFR RAM space 80 – FFH. This is widely used for the new generation of 8051 microcontrollers.

## Slide 23
I/O PROGRAMMING
Using bit Data Type for
Bit-addressable RAM
Write an 8051 C program to get the status of bit P1.0, save it, and send it to P2.7 continuously.
Solution:
#include <reg51.h> sbit inbit=P1^0; sbit outbit=P2^7;
bit membit; //use bit to declare
//bit- addressable memory
//get a bit from P1.0
//send it to P2.7
void main(void)
{
while (1)
{
membit=inbit; outbit=membit;
}
}
We use bit data type to access data in a bit-addressable section of the data RAM space 20 – 2FH

## Slide 24
LOGIC OPERATIONS
Bit-wise Operators in C
Logical operators
  AND (&&), OR (||), and NOT (!)
Bit-wise operators
  AND (&), OR (|), EX-OR (^), Inverter (~), Shift Right (>>), and Shift Left (<<)
    These operators are widely used in software engineering for embedded systems and control
AND OR EX-OR Inverter |  |  |  |  | 
A | B | A&B | A¦B | A^B | ~B
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 0 | 1 | 1 | 
1 | 1 | 1 | 1 | 0 | 
Bit-wise Logic Operators for C

## Slide 25: LOGIC OPERATIONS
Bit-wise Operators in C (cont’)
Run the following program on your simulator and examine the results.
Solution:
#include <reg51.h>
void main(void)
//ANDing
//ORing
//XORing
//inversing
//shifting right 3
//shifting right 4
//shifting left 4
{
P0=0x35 & 0x0F; P1=0x04 | 0x68; P2=0x54 ^ 0x78; P0=~0x55; P1=0x9A >> 3;
P2=0x77 >> 4;
P0=0x6 << 4;
}

## Slide 26: LOGIC OPERATIONS
Bit-wise Operators in C (cont’)
Write an 8051 C program to toggle all the bits of P0 and P2 continuously with a 250 ms delay. Using the inverting and Ex-OR operators, respectively.
Solution:
#include <reg51.h>
void MSDelay(unsigned int);
void main(void)
{
P0=0x55; P2=0x55;
while (1)
{
P0=~P0; P2=P2^0xFF;
MSDelay(250);
}
}

## Slide 27: DATA CONVERSION
Checksum Byte in ROM (cont’)
Write an 8051 C program to perform the checksum operation to ensure data integrity. If data is good, send ASCII character ‘G’ to P0. Otherwise send ‘B’ to P0.
Solution:
#include <reg51.h>
void main(void)
{
unsigned char mydata[]
={0x25,0x62,0x3F,0x52,0xE8};
unsigned char shksum=0; unsigned char x;
for (x=0;x<5;x++) chksum=chksum+mydata[x];
if (chksum==0) P0=‘G’;
else
P0=‘B’;
}