## Slide 1
Embedded Systems Design
Inter-Integrated Circuit (I2C)

## Slide 2: SPI Communication

## Slide 3: SPI clocking: there is no “standard way”
Four clocking “modes”
  Two phases
  Two polarities
Master and selected slave must be in the same mode
During transfers with slaves A and B, Master must
  Configure clock to Slave A’s clock mode
  Select Slave A
  Do transfer
  Deselect Slave A
  Configure clock to Slave B’s clock mode
  Select Slave B
  Do transfer
  Deselect Slave B
Master reconfigures clock mode on-the-fly!

## Slide 4: SPI timing diagram
Timing Diagram – Showing Clock polarities and phases

## Slide 5: SPI Pros and Cons
Pros:
  Fast and easy
    Fast for point-to-point connections
    Easily allows streaming/Constant data inflow
    No addressing/Simple to implement
  Everyone supports it
Cons:
  SS makes multiple slaves very complicated
  No acknowledgement ability
  No inherent arbitration
  No flow control

## Slide 6: I2C bus
Communication with the accelerometer
  Read acceleration values and configure interrupts
Pros
  Two wires bus that can connect multiple peripherals with the MCU
Cons
  Overhead is significantly higher, and bus is slower

## Slide 7: I2C Details
Two lines
  Serial data line (SDA)
  Serial clock line (SCL)
Only two wires for connecting multiple devices

## Slide 8: I2C Details

## Slide 9: I2C Details

## Slide 10: I2C Details
Each I2C device recognized by a unique address
Each I2C device can be either a transmitter or receiver
I2C devices can be masters or slaves for a data transfer
  Master (usually a microcontroller): Initiates a data transfer on the bus, generates the clock signals to permit that transfer, and terminates the transfer
  Slave: Any device addressed by the master at that time

## Slide 11: How can any device transfer or receive on the same two wires?
Pull ups and high-impedance mode pins
  Wires default to being “on”, any device can make a wire go “off”.
  This is super clever. SPI and UART can’t do this, why?

## Slide 12: Start and Stop Condition

## Slide 13: Acknowledge (ACK) and Not Acknowledge (NACK)
A transition of the data line while the clock line is high
is defined as either a start
or a stop condition.
Both start and stop conditions are generated by the bus master
The bus is considered busy after a start condition, until a stop condition occurs

## Slide 14: Bit Transfer on the I2C Bus

## Slide 15: Start and Stop Conditions
A transition of the data line while the clock line is high is defined as either a start or a stop condition.
Both start and stop conditions are generated by the bus master
The bus is considered busy after a start condition, until a stop condition occurs
Start Condition
Stop Condition
SCL
SCL
SDA
SDA

## Slide 16: I2C Addressing
Each node has a unique 7 (or 10) bit address
Peripherals often have fixed and programmable address portions
Addresses starting with 0000 or 1111 have special functions:-
  0000000 Is a General Call Address
  0000001 Is a Null (CBUS) Address

## Slide 17: I2C-Connected System
Example I2C-connected system with two microcontrollers
(Source: I2C Specification, Philips)

## Slide 18: Master-Slave Relationships
Who is the master?
  master-transmitters
  master-receivers
Suppose microcontroller A wants to send information to microcontroller B
  A (master) addresses B (slave)
  A (master-transmitter), sends data to B (slave-receiver)
  A terminates the transfer.
If microcontroller A wants to receive information from microcontroller B
  A (master) addresses microcontroller B (slave)
  A (master-receiver) receives data from B (slave-transmitter)
  A terminates the transfer
In both cases, the master (microcontroller A) generates the timing and terminates the transfer

## Slide 19: Read and Write Operation in I2C

## Slide 20: I2C protocol
Master initiates transfer with a START bit (SDA from high to low while SCL is high
Slave address (7 or 10 bits, 7 is most common)
Transfer type (1 bit: 0 to write, 1 to read)
  All ICs compare address to their address
    If address matches, device sends an ACKNOWLEDGE signal
    If address does not match, device waits until bus is released by STOP condition
Once master receives ACKNOWLEDGE, it then sends (writes) or receives (reads) data
  Receiver sends back ACKNOWLEDGE for each byte received
Master concludes the transfer with STOP bit
General structure of a 2-byte transfer
Writing 2-bytes (shaded bits are put on the bus by the master)
Reading 2-bytes (shaded bits are put on the bus by the master)
http://www.robot-electronics.co.uk/acatalog/I2C_Tutorial.html