## Slide 1: ARITHMETIC & LOGIC INSTRUCTIONS AND PROGRAMS
The 8051 Microcontroller and Embedded Systems: Using Assembly and C

## Slide 2: ADD A,source ;A = A + source
ARITHMETIC INSTRUCTIONS
Addition of Unsigned Numbers
The instruction ADD is used to add two operands
  Destination operand is always in register A
  Source operand can be a register, immediate data, or in memory
  Memory-to-memory arithmetic operations are never allowed in 8051 Assembly language
Show how the flag register is affected by the following instruction.
MOV A,#0F5H ;A=F5 hex ADD A,#0BH ;A=F5+0B=00
Solution:
F5H 1111 0101
+ 0BH + 0000 1011
100H 0000 0000
CY =1, since there is a carry out from D7
PF =1, because the number of 1s is zero (an even number), PF is set to 1.
AC =1, since there is a carry from D3 to D4
2

## Slide 3
ARITHMETIC INSTRUCTIONS
ADDC and Addition of 16- Bit Numbers
When adding two 16-bit data operands, the propagation of a carry from lower byte to higher byte is concerned
Write a program to add two 16-bit numbers. Place the sum in R7 and R6; R6 should have the lower byte.
Solution:
CLR | C |  | ;make CY=0 | 
MOV | A, | #0E7H | ;load the low byte now A=E7H | 
ADD | A, | #8DH | ;add the low byte | 
MOV | R6, A |  | ;save the | low byte sum in R6
MOV | A, #3CH |  | ;load the | high byte
ADDC | A, #3BH |  | ;add with | the carry
MOV | R7, A |  | ;save the | high byte sum
When the first byte is added (E7+8D=74, CY=1).
The carry is propagated to the higher byte, which result in 3C
+ 3B + 1 =78 (all in hex)
3
1
3C E7
+ 3B 8D
78 74

## Slide 4: DA A ;decimal adjust for addition
ARITHMETIC INSTRUCTIONS
DA Instruction
The DA instruction is provided to correct the aforementioned problem associated with BCD addition
  The DA instruction will add 6 to the lower nibble or higher nibble if need
DA works only after an ADD, but not after INC
Example: | 6CH | 
MOV A,#47H ;A=47H first BCD operand MOV B,#25H ;B=25H second BCD operand ADD A,B ;hex(binary) addition(A=6CH) DA A ;adjust for BCD addition 72H (A=72H) The “DA” instruction works only on A. In other word, while the source can be an operand of any addressing mode, the destination must be in register A in order for DA to work. |  | 

## Slide 5
ARITHMETIC INSTRUCTIONS
DA Instruction
(cont’)
Summary of DA instruction
After an ADD or ADDC instruction
  If the lower nibble (4 bits) is greater than 9, or if AC=1, add 0110 to the lower 4 bits
  If the upper nibble is greater than 9, or if CY=1, add 0110 to the upper 4 bits
Example:
 | HEX |  | BCD | 
 | 29 |  | 0010 1001 | 
+ | 18 | + | 0001 1000 | 
 | 41 |  | 0100 0001 | AC=1
+ | 6 | + | 0110 | 
 | 47 |  | 0100 0111 | 
Since AC=1 after the
addition, ”DA A” will add 6 to the lower nibble.
The final result is in BCD format.

## Slide 6
ARITHMETIC INSTRUCTIONS
Subtraction of Unsigned Numbers
In many microprocessor there are two different instructions for subtraction: SUB and SUBB (subtract with borrow)
  In the 8051 we have only SUBB
  The 8051 uses adder circuitry to perform the subtraction
SUBB A,source ;A = A – source – CY
To make SUB out of SUBB, we have to make CY=0 prior to the execution of the instruction
  Notice that we use the CY flag for the borrow

## Slide 7
ARITHMETIC INSTRUCTIONS
Subtraction of Unsigned Numbers (cont’)
SUBB when CY = 0
Take the 2’s complement of the subtrahend (source operand)
Add it to the minuend (A)
Invert the carry
;load A with value 4CH
;subtract 6E from A
;if CY=0 jump to NEXT
A ;if CY=1, take 1’s complement A ;and increment to get 2’s comp
CLR C
MOV A,#4C
SUBB A,#6EH
JNC NEXT CPL
INC MOV
R1,A ;save A in R1
NEXT:
Solution:
4C | 0100 | 1100 | 0100 1100
- 6E | 0110 | 1110 | 1001 0010
-22 |  |  | 01101 1110
CY =1
 +
 2’s complement
 Invert carry
CY=0, the result is positive; CY=1, the result is negative and the destination has the 2’s complement of the result

## Slide 8
ARITHMETIC INSTRUCTIONS
Subtraction of Unsigned Numbers (cont’)
SUBB when CY = 1
  This instruction is used for multi-byte numbers and will take care of the borrow of the lower operand
CLR C
;A=62H
MOV A,#62H
SUBB A,#96H
MOV R7,A
MOV A,#27H
SUBB A,#12H
MOV R6,A
;62H-96H=CCH with CY=1
;save the result
;A=27H
;27H-12H-1=14H
;save the result
Solution:
We have 2762H - 1296H = 14CCH.
A = 62H – 96H – 0 = CCH
CY = 1
A = 27H - 12H - 1 = 14H CY = 0

## Slide 9
ARITHMETIC INSTRUCTIONS
Unsigned Multiplication
The 8051 supports byte by byte multiplication only
  The byte are assumed to be unsigned data
MUL AB ;AxB, 16-bit result in B, A
MOV | A,#25H | ;load 25H to | reg. | A
MOV | B,#65H | ;load 65H to | reg. | B
MUL | AB | ;25H * 65H = ;B = OEH and | E99 where A = 99H | 
Unsigned Multiplication Summary (MUL AB) |  |  |  |  | 
 | Multiplication | Operand1 | Operand2 | Result | 
 | Byte x byte | A | B | B = high byte A = low byte | 

## Slide 10
ARITHMETIC INSTRUCTIONS
Unsigned Division
The 8051 supports byte over byte division only
  The byte are assumed to be unsigned data
DIV AB ;divide A by B, A/B
MOV | A,#95 | ;load 95 to | reg. | A
MOV | B,#10 | ;load 10 to | reg. | B
MUL
AB
;A = 09(quotient) and
;B = 05(remainder)
Division | Numerator | Denominator | Quotient | Remainder
Byte / byte | A | B | A | B
Unsigned Division Summary (DIV AB)
CY is always 0 If B  0, OV = 0
If B = 0, OV = 1 indicates error

## Slide 11
SIGNED ARITHMETIC INSTRUCTIONS
D7 (MSB) is the sign and D0 to D6 are the magnitude of the number
  If D7=0, the operand is positive, and if D7=1, it is negative
Signed 8-bit Operands
Sign Magnitude
Positive numbers are 0 to +127
Negative number representation (2’s complement)
  Write the magnitude of the number in 8-bit binary (no sign)
  Invert each bit
  Add 1 to it
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0

## Slide 12: SIGNED ARITHMETIC INSTRUCTIONS
Signed 8-bit Operands (cont’)
Show how the 8051 would represent -34H
Solution:
0011 0100 34H given in binary
1100 1011 invert each bit
1100 1100 add 1 (which is CC in hex)
Signed number representation of -34 in 2’s complement is CCH
Decimal | Binary |  | Hex
-128 | 1000 | 0000 | 80
-127 | 1000 | 0001 | 81
-126 | 1000 | 0010 | 82
... | ... ... |  | ...
-2 | 1111 | 1110 | FE
-1 | 1111 | 1111 | FF
0 | 0000 | 0000 | 00
+1 | 0000 | 0001 | 01
+2 | 0000 | 0010 | 02
... | ... ... |  | ...
+127 | 0111 | 1111 | 7F

## Slide 13
SIGNED ARITHMETIC INSTRUCTIONS
Overflow Problem
Examine the following code and analyze the result.
MOV MOV ADD |  | A,#+96 R1,#+70 A,R1 |  |  | ;A=0110 0000 (A=60H) ;R1=0100 0110(R1=46H) ;A=1010 0110 ;A=A6H=-90,INVALID
Solution: |  |  |  |  | 
 | +96 |  | 0110 | 0000 | 
+ | +70 |  | 0100 | 0110 | 
+ | 166 |  | 1010 | 0110 | and OV =1
According to the CPU, the result is -90, which is wrong. The CPU sets OV=1 to indicate the overflow
If the result of an operation on signed numbers is too large for the register
  An overflow has occurred and the programmer must be noticed

## Slide 14
SIGNED ARITHMETIC INSTRUCTIONS
OV Flag
In 8-bit signed number operations, OV is set to 1 if either occurs:
There is a carry from D6 to D7, but no carry out of D7 (CY=0)
There is a carry from D7 out (CY=1), but no carry from D6 to D7
MOV MOV ADD | A,#-128 R4,#-2 A,R4 |  | ;A=1000 0000(A=80H) ;R4=1111 1110(R4=FEH) ;A=0111 1110(A=7EH=+126,INVALID) |  | 
 | -128 |  |  | 1000 | 0000
+ | -2 |  |  | 1111 | 1110
 | -130 |  |  | 0111 | 1110 and OV=1
OV = 1
The result +126 is wrong

## Slide 15
SIGNED ARITHMETIC INSTRUCTIONS
OV Flag
(cont’)
MOV A,#-2 MOV R1,#-5 ADD A,R1
-2
+ -5
;A=1111 1110(A=FEH)
;R1=1111 1011(R1=FBH)
;A=1111 1001(A=F9H=-7,
;Correct, OV=0)
1111 1110
1111 1011
-7
1111 1001 and OV=0
OV = 0
The result -7 is correct
MOV A,#+7 MOV R1,#+18 ADD A,R1
7
+ 18 25
;A=0000 0111(A=07H)
;R1=0001 0010(R1=12H)
;A=0001 1001(A=19H=+25,
;Correct,OV=0)
0000 0111
0001 0010
0001 1001 and OV=0
OV = 0
The result +25 is correct

## Slide 16
SIGNED ARITHMETIC INSTRUCTIONS
OV Flag
(cont’)
In unsigned number addition, we must monitor the status of CY (carry)
  Use JNC or JC instructions
In signed number addition, the OV (overflow) flag must be monitored by the programmer
  JB PSW.2 or JNB PSW.2

## Slide 17
SIGNED ARITHMETIC INSTRUCTIONS
2's Complement
To make the 2’s complement of a number
CPL ADD
A A,#1
;1’s complement (invert)
;add 1 to make 2’s comp.

## Slide 18: ANL destination,source
LOGIC AND COMPARE INSTRUCTIONS
AND
;dest = dest AND source
This instruction will perform a logic AND on the two operands and place the result in the destination
  The destination is normally the accumulator
  The source operand can be a register, in memory, or immediate
X Y X AND Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Show the results of the following.
MOV A,#35H ANL A,#0FH
;A = 35H
;A = A AND 0FH
35H | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1
0FH | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
05H | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
ANL is often used to mask (set to 0) certain bits of an operand

## Slide 19: ORL destination,source
LOGIC AND COMPARE INSTRUCTIONS OR |  | 
X | Y | X OR Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
;dest = dest OR source
The destination and source operands are ORed and the result is placed in the destination
  The destination is normally the accumulator
  The source operand can be a register, in memory, or immediate
Show the results of the following.
MOV A,#04H ORL A,#68H
;A = 04
;A = 6C
04H | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
68H | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0
6CH | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0
ORL instruction can be used to set certain bits of an operand to 1

## Slide 20: XRL destination,source
LOGIC AND COMPARE INSTRUCTIONS
XOR
;dest = dest XOR source
This instruction will perform XOR operation on the two operands and place the result in the destination
  The destination is normally the accumulator
  The source operand can be a register, in memory, or immediate
Show the results of the following.
MOV A,#54H XRL A,#78H
X Y X XOR Y
0 0
0
0 1
1
1 0
1
1 1
0
XRL instruction can be
54H | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | used to toggle certain
78H | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | bits of an operand
2CH | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 

## Slide 21: LOGIC AND COMPARE INSTRUCTIONS
Department of Computer Scie
nce and Information Engineering
National Cheng Kung University, TAIWAN
26
HANEL
XOR
(cont’)
The XRL instruction can be used to clear the contents of a register by XORing it with itself. Show how XRL A,A clears A, assuming that AH = 45H.
45H
45H
00H
0 1 0 0 0 1 0 1
0 1 0 0 0 1 0 1
0 0 0 0 0 0 0 0
Read and test P1 to see whether it has the value 45H. If it does, send
99H to P2; otherwise, it stays cleared.
Solution:
;clear P2
;make P1 an input port
;R3=45H
;read P1
;jump if A is not 0
MOV P2,#00 MOV P1,#0FFH MOV R3,#45H MOV A,P1 XRL A,R3 JNZ EXIT
MOV P2,#99H
EXIT: ...
XRL can be used to see if two registers have the same value
If both registers have the same value, 00 is placed in A. JNZ
and JZ test the contents of the
accumulator.

## Slide 22: CPL A ;complements the register A
LOGIC AND COMPARE INSTRUCTIONS
Complement Accumulator
This is called 1’s complement
To get the 2’s complement, all we have to do is to to add 1 to the 1’s complement
MOV A, #55H CPL A
;now A=AAH
;0101 0101(55H)
;becomes 1010 1010(AAH)

## Slide 23: RR A ;rotate right A
ROTATE INSTRUCTION AND DATA SERIALIZATION
Rotating Right and Left
In rotate right
  The 8 bits of the accumulator are rotated right one bit, and
  Bit D0 exits from the LSB and enters into MSB, D7
MSB
LSB
MOV | A,#36H | ;A | = | 0011 | 0110
RR | A | ;A | = | 0001 | 1011
RR | A | ;A | = | 1000 | 1101
RR | A | ;A | = | 1100 | 0110
RR | A | ;A | = | 0110 | 0011

## Slide 24: RL A ;rotate left A
ROTATE INSTRUCTION AND DATA SERIALIZATION
Rotating Right and Left (cont’)
In rotate left
  The 8 bits of the accumulator are rotated left one bit, and
  Bit D7 exits from the MSB and enters into LSB, D0
MSB
LSB
MOV | A,#72H | ;A | = | 0111 | 0010
RL | A | ;A | = | 1110 | 0100
RL | A | ;A | = | 1100 | 1001

## Slide 25: RRC A ;rotate right through carry
ROTATE INSTRUCTION AND DATA SERIALIZATION
Rotating through Carry
In RRC A
  Bits are rotated from left to right
  They exit the LSB to the carry flag, and the carry flag enters the MSB
MSB LSB
CLR C
;make CY = 0
MOV | A,#26H | ;A | = | 0010 | 0110 |  |  | 
RRC | A | ;A | = | 0001 | 0011 | CY | = | 0
RRC | A | ;A | = | 0000 | 1001 | CY | = | 1
RRC | A | ;A | = | 1000 | 0100 | CY | = | 1
CY

## Slide 26: RLC A ;rotate left through carry
ROTATE INSTRUCTION AND DATA SERIALIZATION
Rotating through Carry (cont’)
In RLC A
  Bits are shifted from right to left
  They exit the MSB and enter the carry flag, and the carry flag enters the LSB
MSB LSB
CY
Write a program that finds the number of 1s in a given byte. |  | 
MOV | R1,#0 | 
MOV | R7,#8 | ;count=08
MOV | A,#97H | 
AGAIN: RLC | A | 
JNC | NEXT | ;check for CY
INC | R1 | ;if CY=1 add to count
NEXT: DJNZ | R7,AGAIN | 

## Slide 27
ROTATE INSTRUCTION AND DATA SERIALIZATION
Serializing Data
Serializing data is a way of sending a byte of data one bit at a time through a single pin of microcontroller
  Using the serial port, discussed in Chapter 10
  To transfer data one bit at a time and control the sequence of data and spaces in between them

## Slide 28
ROTATE INSTRUCTION AND DATA SERIALIZATION
Serializing Data
(cont’)
Transfer a byte of data serially by
  Moving CY to any pin of ports P0 – P3
  Using rotate instruction
Write a program to transfer value 41H serially (one bit at a time) via pin P2.1. Put two highs at the start and end of the data. Send the byte LSB first.
;high
;high
Solution:
MOV SETB SETB MOV
AGAIN: RRC
MOV DJNZ SETB SETB
A,#41H P2.1 P2.1 R5,#8 A P2.1,C R5,HERE P2.1 P2.1
P2.1
CY
 | Register A | 
D7
D0
;send CY to P2.1
;high
;high
Pin

## Slide 29: ROTATE INSTRUCTION AND DATA SERIALIZATION
Serializing Data
(cont’)
Write a program to bring in a byte of data serially one bit at a time via pin P2.7 and save it in register R2. The byte comes in with the LSB first.
Solution:
MOV AGAIN: MOV RRC DJNZ MOV | R5,#8 C,P2.7 A R5,HERE R2,A | ;bring in bit ;save it |  | 
Pin |  |  |  | 
P2.7 | CY |  | Register A | 
 |  | D7 D0 |  | 

## Slide 30
ROTATE INSTRUCTION AND DATA SERIALIZATION
Single-bit Operations with CY
There are several instructions by which the CY flag can be manipulated directly
Instruction |  | Function
SETB | C | Make CY = 1
CLR | C | Clear carry bit (CY = 0)
CPL | C | Complement carry bit
MOV | b,C | Copy carry status to bit location (CY = b)
MOV | C,b | Copy bit location status to carry (b = CY)
JNC | target | Jump to target if CY = 0
JC | target | Jump to target if CY = 1
ANL | C,bit | AND CY with bit and save it on CY
ANL | C,/bit | AND CY with inverted bit and save it on CY
ORL | C,bit | OR CY with bit and save it on CY
ORL | C,/bit | OR CY with inverted bit and save it on CY

## Slide 31: ROTATE INSTRUCTION AND DATA SERIALIZATION
Single-bit Operations with CY
(cont’)
Assume that bit P2.2 is used to control an outdoor light and bit P2.5 a light inside a building. Show how to turn on the outside light and turn off the inside one.
Solution:
SETB | C | ;CY = | 1
ORL | C,P2.2 | ;CY = | P2.2 ORed w/ CY
MOV | P2.2,C | ;turn | it on if not on
CLR | C | ;CY = | 0
ANL | C,P2.5 | ;CY = | P2.5 ANDed w/ CY
MOV P2.5,C ;turn it off if not off
Write a program that finds the number of 1s in a given byte.
Solution:
R1,#0 ;R1 keeps number of 1s
R7,#8 ;counter, rotate 8 times
MOV MOV MOV
AGAIN: RLC
JNC INC
A,#97H ;find number of 1s in 97H A
NEXT R1
NEXT: DJNZ R7,AGAIN
;rotate it thru CY
;check CY
;if CY=1, inc count
;go thru 8 times

## Slide 32: SWAP A
ROTATE INSTRUCTION AND DATA SERIALIZATION
SWAP
It swaps the lower nibble and the higher nibble
  In other words, the lower 4 bits are put into the higher 4 bits and the higher 4 bits are put into the lower 4 bits
SWAP works only on the accumulator (A)
D7-D4
before :
after :
D3-D0
D3-D0
D7-D4

## Slide 33: ROTATE INSTRUCTION AND DATA SERIALIZATION
SWAP
(cont’)
Find the contents of register A in the following code.
In the absence of a SWAP instruction, how would you exchange the nibbles? Write a simple program to show the process.
Solution:
(a)
MOV A,#72H
SWAP A
;A = 72H
;A = 27H
(b)
MOV RL RL RL RL
A,#72H A
A
A A
;A = 0111 0010
;A = 0111 0010
;A = 0111 0010
;A = 0111 0010
;A = 0111 0010

## Slide 34
BCD AND ASCII APPLICATION PROGRAMS
Checksum Byte in ROM (cont’)
To calculate the checksum byte of a series of bytes of data
  Add the bytes together and drop the carries
  Take the 2’s complement of the total sum, and it becomes the last byte of the series
To perform the checksum operation, add all the bytes, including the checksum byte
  The result must be zero
  If it is not zero, one or more bytes of data have been changed

## Slide 35: BCD AND ASCII APPLICATION PROGRAMS
Checksum Byte in ROM (cont’)
Assume that we have 4 bytes of hexadecimal data: 25H, 62H, 3FH, and 52H.(a) Find the checksum byte, (b) perform the checksum operation to ensure data integrity, and (c) if the second byte 62H has been changed to 22H, show how checksum detects the error.
Solution:
(a) Find the checksum byte.
25H
+ 62H
+ 3FH
+ 52H
The checksum is calculated by first adding the bytes. The sum is 118H, and dropping the carry, we get 18H. The checksum byte is the 2’s complement of 18H, which is E8H
118H
(b) Perform the checksum operation to ensure data integrity. 25H
+ 62H Adding the series of bytes including the checksum
+ 3FH
+ 52H
byte must result in zero. This indicates that all the bytes are unchanged and no byte is corrupted.
+ E8H
200H (dropping the carries)
(c) If the second byte 62H has been changed to 22H, show how checksum detects the error.
25H
+ 22H Adding the series of bytes including the checksum
+ 3FH
+ 52H
byte shows that the result is not zero, which indicates that one or more bytes have been corrupted.
+ E8H
1C0H (dropping the carry, we get C0H)