## Slide 1: Computer System Overview
Covers Chapter#01 from Textbook

## Slide 2: Outline
Operating System
Example of Instruction Execution
The Memory Hierarchy
Interrupts
Basic Elements of Computer System
Instruction Execution

## Slide 3: Interrupts
Interrupt: a mechanism by which other modules (I/O, memory) may interrupt the normal sequencing of the processor.
Main benefit: interrupts are provided primarily as a way to improve processor utilization.
The classes of Interrupts are:
Program | Generated by a condition that occurs as a result of an instruction execution, such as arithmetic overflow, division by zero, attempt to execute an illegal machine instruction, and reference outside a user’s allowed memory space.
Timer | Generated by a timer within the processor.
I/O | Generated by an I/O controller, to signal normal completion of an operation or to signal a variety of error conditions.
Hardware failure | Generated by a failure, such as memory parity error.

## Slide 4
Figure 1.5 Program Flow of Control Without and With Interrupts

## Slide 5: Interrupts (Cont.)
No interrupts scenario:
The “user program” performs a series of WRITE calls.
The WRITE calls are to an “I/O routine” that is a “system utility” and that will perform the actual “I/O operation”.
After the first WRITE instruction is encountered, the “user program” is interrupted and execution continues with “I/O program”.
After “I/O program” execution is complete, execution resumes in the “user program” immediately following the WRITE instruction.
Since “I/O operation” may take a relatively long time to complete, the “I/O program” is hung up waiting for the operation to complete. Hence, the “user program” is stopped at the point of the WRITE call for some considerable period of time.

## Slide 6: Interrupts (Cont.)
Interrupts; short I/O wait scenario:
With interrupts, the processor can be engaged in executing other instructions while an I/O operation is in progress.
The I/O operation is conducted concurrently with the execution of instructions in the user program.
When the external device becomes ready to accept more data from the processor, the I/O module for that external device sends an interrupt request signal to the processor.
The processor responds by suspending operation of the current program; branching off to a routine to service that particular I/O device, known as an interrupt handler; and resuming the original execution after the device is serviced.

## Slide 7: Interrupts (Cont.)
Interrupts; short I/O wait scenario (Cont.):
Because of the relatively large amount of time that would be wasted by simply waiting on an I/O operation, the processor can be employed much more efficiently with use of interrupts.
Interrupts; long I/O wait scenario:
The user program reaches the second WRITE call before the I/O operation spawned by the first call is complete. The user program is hung up at that point.
When the preceding I/O operation is completed, this new WRITE call may be processed, and a new I/O operation may be started.

## Slide 8: Interrupts (Cont.)

## Slide 9: Multiple Interrupts
Two approaches can be taken to deal with multiple interrupts:
To disable interrupts while an interrupt is being processed.
  The processor ignores any new interrupt request signal.
  If an interrupt occurs, it generally remains pending and will be checked by processor after the processor has reenabled interrupts.
  Interrupts are handled in strict sequential order.
  Drawback is the lack of taking into account relative priority or time-critical needs.
Define priorities for interrupts and allow an interrupt of higher priority to cause a lower-priority interrupt handler to be interrupted.

## Slide 10: Multiple Interrupts (Cont.)

## Slide 11
Printer, priority = 2.
Disk, priority = 4.
Comm line, priority = 5.
t = 0, user program begins.
t = 10, printer interrupt.
t = 15, comm interrupt.
t = 20, disk interrupt.

## Slide 12: The Memory Hierarchy
The design constraints on a computer’s memory can be summed up by three questions: How much? How fast? How expensive?
There is a trade-off among the three key characteristics of memory: namely, capacity, access time, and cost.
A variety of technologies are used to implement memory systems, where the following relationships hold:
  Faster access time, greater cost per bit.
  Greater capacity, smaller cost per bit.
  Greater capacity, slower access speed.
The way to meet both large capacity and performance is to employ a memory hierarchy.

## Slide 13: The Memory Hierarchy (Cont.)
Going down the hierarchy, the following occurs:
Decreasing cost per bit.
Increasing capacity.
Increasing access time.
Decreasing frequency of access to the memory by the processor.

## Slide 14: Thank You!